## Sub-conjunto de instruções do MIPS

| Grupo | Sintaxe | Tipo | Op | Func | Comentário |
| --- | --- | --- | --- | --- | --- |
|  | lb Rdest, Imm16(Rsrc) | I | 0x20 | - | load byte |
|  | lw Rdest, Imm16(Rsrc) | I | 0x23 | - | load word |
|  | lbu Rdest, Imm16(Rsrc) | I | 0x24 | - | load unsigned byte |
|  | sb Rsrc2, Imm16(Rsrc1) | I | 0x28 | - | store byte |
|  | sw Rsrc2, Imm16(Rsrc1) | I | 0x2b | - | store word |
| Transferência | lui Rdest, Imm16 | I | 0x0f | - | load upper immediate |
| de | mfhi Rdest | R | 00 | 0x10 | move from hi |
| informação | mflo Rdest | R | 00 | 0x12 | move from lo |
|  | mthi Rsrc | R | 00 | 0x11 | move to hi |
|  | mtlo Rsrc | R | 00 | 0x13 | move to lo |
|  | li Rdest, Imm16/32 |  |  |  | load immediate |
|  | la Rdest, address16/32 |  |  |  | load address |
|  | move Rdest, Rsrc |  |  |  | move |
|  | add Rdest, Rsrc1, Rsrc2 | R | 00 | 0x20 | addition (with overflow) |
|  | addi Rdest, Rsrc, Imm16 | I | 08 | - | addition imm. (with ov.) |
|  | addu Rdest, Rsrc1, Rsrc2 | R | 00 | 0x21 | addition (without overflow) |
|  | addiu Rdest, Rsrc, Imm16 | I | 09 | - | addition imm. (without ov.) |
|  | sub Rdest, Rsrc1, Rsrc2 | R | 00 | 0x22 | subtract (with overflow) |
|  | subu Rdest, Rsrc1, Rsrc2 | R | 00 | 0x23 | subtract (without overflow) |
| Operações | mult Rsrc1, Rsrc2 | R | 00 | 0x18 | multiply |
| aritméticas | multu Rsrc1, Rsrc2 | R | 00 | 0x19 | unsigned multiply |
|  | div Rsrc1, Rsrc2 | R | 00 | 0x1a | divide |
|  | divu Rsrc1, Rsrc2 | R | 00 | 0x1b | unsigned divide |
|  | abs Rdest, Rsrc |  |  |  | absolute value |
|  | mul Rdest, Rsrc1, Rsrc2 |  |  |  | multiply |
|  | div Rdest, Rsrc1, Rsrc2 |  |  |  | divide |
|  | rem Rdest, Rsrc1, Rsrc2 |  |  |  | remainder |
|  | and Rdest, Rsrc1, Rsrc2 | R | 00 | 0x24 | AND |
|  | andi Rdest, Rsrc, Imm16 | I | 0x0c | - | AND immediate |
|  | or Rdest, Rsrc1, Rsrc2 | R | 00 | 0x25 | OR |
|  | ori Rdest, Rsrc, Imm16 | I | 0x0d | - | OR immediate |
| Operações | xor Rdest, Rsrc1, Rsrc2 | R | 00 | 0x26 | XOR |
| lógicas | xori Rdest, Rsrc, Imm16 | I | 0x0e | - | XOR immediate |
| e de | nor Rdest, Rsrc1, Rsrc2 | R | 00 | 0x27 | NOR |
| comparação | slt Rdest, Rsrc1, Rsrc2 | R | 00 | 0x2a | set on less than |
|  | slti Rdest, Rsrc, Imm16 | I | 0x0a | - | set on less than immediate |
|  | sltu Rdest, Rsrc1, Rsrc2 | R | 00 | 0x2b | set on less than unsigned |
|  | sltiu Rdest, Rsrc, Imm16 | I | 0x0b | - | set on less than unsigned imm. |
|  | not Rdest, Rsrc |  |  |  | not |
|  | sll Rdest, Rsrc, Shamt5 | R | 00 | 00 | shift left logical |
| Operações de | srl Rdest, Rsrc, Shamt5 | R | 00 | 02 | shift right logical |
| deslocamento | sra Rdest, Rsrc, Shamt5 | R | 00 | 03 | shift right arithmetic |
| de bits | rol Rdest, Rsrc1, Rsrc2 |  |  |  | rotate left |
|  | ror Rdest, Rsrc1, Rsrc2 |  |  |  | rotate right |
|  | j address28 | J | 02 | - | jump (absolute addr) |
|  | jr Rsrc | R | 00 | 08 | jump register |
|  | beq Rsrc1, Rsrc2, address18 | I | 04 | - | branch on equal (relative addr) |
|  | bne Rsrc1, Rsrc2, address18 | I | 05 | - | branch on not equal (relative addr) |
| Instruções | bgez Rsrc, address18 | I | 01 | 01* | br. on greater than equal zero ( “ ” ) |
| de salto | bgtz Rsrc, address18 | I | 07 | - | br. on greater than zero ( “ ” ) |
|  | blez Rsrc, address18 | I | 06 | - | br. on less than equal zero ( “ ” ) |
|  | bltz Rsrc, address18 | I | 01 | 00* | br. on less than zero ( “ ” ) |
|  | jal address28 | J | 03 | - | jump and link (absolute addr) |
|  | jalr Rsrc | R | 00 | 09 | jump and link register |
|  | b address18/32 |  |  |  | branch inconditional (relative addr) |
|  | b<cnd> Rsrc1, Rsrc2, address18/32 |  |  |  | br. on <cnd> = [gt, ge, lt, le] ( “ ” ) |
|  | b<cnd>u Rsrc1, Rsrc2, address18/32 |  |  |  | br. on <cnd> = [gt, ge, lt, le] uns. ( “ ” ) |
|  | rfe | R | 0x10 | 0x20 | return from exception |
| Excepção | syscall | R | 00 | 0x0c | system call |
|  | break code20 | R | 00 | 0x0d | break |

* especificado no campo rt

Formatos das instruções e exemplos

| Instrução | Tipo | Op/6 bits | Rs/5 bits | Rt/5 bits | Rd/5 bits | Sa/5 bits | Func/6 bits |
| --- | --- | --- | --- | --- | --- | --- | --- |
| add $a0, $t0, $s0 | R | 0 | 8 ($t0) | 0x10 ($s0) | 4 ($a0) | 0 | 0x20 |
| addi $8, $9, 0x100 | I | 8 | 9 | 8 | 0x100 |
| sw $6, -4 ($7) | I | 0x2b | 7 | 6 | 0xfffc (-4) |
| beq $4, $5, 0x60 | I | 4 | 4 | 5 | 0x18 (0x60/4) |
| j 0x80000 | J | 2 | 0x20000 (0x80000/4) |